## Slide 1
תרגול 3
פונקציות
Maroun Tork, 2018

## Slide 2
Register Names
Name | Reg # | Use | Saver
X0 | 0 | Constant 0 | -
ra | 1 | Return Address | Caller
sp | 2 | Stack Pointer | Callee
gp | 3 | Global Pointer | -
tp | 4 | Thread Pointer | -
t0-t2 | 5-7 | Temp | Caller
s0-s1 | 8-9 | Saved Registers | Callee
a0-a7 | 10-17 | Function arguments/ return values (0-1) | Caller
s2-s11 | 18-27 | Saved Registers | Callee
t3-t6 | 28-31 | Temp | Caller

## Slide 3
Pre-call
גיבוי רגיסטרים שלא נשמרים (ti, ai, ra) למחסנית
הכנת ארגומנטים לפונקציה ב- a0-a7
העברת שליטה לפונקציה ושמירת כתובת החזרה ב- ra ע"י jal
Post-call
שחזור רגיסטרים שלא נשמרים (ti, ai, ra) מהמחסנית
Prologue
הקצאת זיכרון מחסנית ע"י הקטנת sp
גיבוי רגיסטרים "שמורים" si
תוכן הפונקציה
Epilogue
הכנת ערכי החזרה ב- a0,a1
שחזור רגיסטרים שמורים si מהמחסנית
שחרור הזיכרון שהוקצה ע"י הגדלת sp
החזרת שליטה לפונקציה הקוראת ע"י jr ra
פונקציה נקראת
פונקציה קוראת
פונקציה קוראת
pre-call
call
post-call
prologue
Function
Body
epilogue

## Slide 4
זיכרון
SP=0x2014
0x2014
0x2010
0x200c
0x2008
0x2004
0x2000
בתחילת ריצת הפונקציה (prologue) עדיין לא נוכל לכתוב למחסנית. הכתובת שאליה מצביע sp שייכת לפונקציה אחרת (הקוראת)
לא שלנו!
כדי להקצות מקום נקטין את :sp
addi sp, sp, -8
SP=0x200c
שלנו
שלנו
כעת לפונקציה שלנו יש הקצאת זיכרון בגודל 8 בתים (שתי מילים). נוכל להשתמש בזיכרון לצרכי הפונקציה. למשל גיבוי s0 ו- s1:
sw s0, 0(sp)
sw s1, 4(sp)
s0
s1
בסיום ריצת הפונקציה (epilogue), נחזיר את sp לערכו המקורי (אין צורך לאפס את המידע שכתבנו למחסנית)
addi sp, sp, 8
s0
s1

## Slide 5: Fundamental steps in calling a function
Caller pre-call:
1- Caller saves the registers which are not preserved on call, which will be needed for farther use after the return from the called function. (arguments/return registers a0-a7, ra, “temporary registers” t0-t6).
2- Caller puts parameters in a place where function can access them (Registers a0-a7).
3- Caller saves the address of next instruction to register ra (return address) and then transfers the control to the function by jumping to the function’s code (using jal).

## Slide 6: Fundamental steps in calling a function
Callee prologue:
1- The called function (callee) acquires local storage (stack) resources needed, by decrementing the sp.
2- The called function (callee) stores preserved on call registers (“saved registers” s0-s11) that will be used by the function in the stack.

## Slide 7: Fundamental steps in calling a function
The function performs the desired tasks

## Slide 8: Fundamental steps in calling a function
Callee epilogue:
1- The called function (callee) puts the result values in the registers a0-a1 where calling code can access it.
2- The function restores any registers it used from the preserved on call registers.
3- The function frees the local storage, by incrementing the sp.
4- The function returns the control to point of origin of the caller (according to register ra, using jr).

## Slide 9: Fundamental steps in calling a function
Caller post-call:
1- Caller restores the registers which are not preserved on call which it stored previous to the call. (arguments/return registers a0-a7, ra, “temporary registers” t0-t6).

## Slide 10: Questions
A. How do we pass arguments into functions?
Use the 8 arguments registers a0 – a7
B. How are values returned by functions?
Use a0 and a1 as the return value registers
C. What is sp and how should it be used in the context of RISC-V functions?
sp stands for stack pointer. We subtract from sp to create more space and add to free space. The stack is mainly used to save (and later restore) the value of registers that may be overwritten.

## Slide 11: Questions
D. Which values need to be saved before using jal?
Registers a0 – a7, t0 – t6, and ra
E. Which values need to be restored before using jr to return from a function?
Registers sp, gp, tp, and s0 – s11

## Slide 12: Example
... sum(a,b);... /* a,b:s0,s1 */ int sum(int x, int y) { return x+y; }
address (shown in decimal) 1000 1004 1008 1012 1016 … 2000 2004
In RISC-V, all instructions are 4 bytes, and stored in memory just like data. So here we show the addresses of where the programs are stored.

## Slide 13
... sum(a,b);... /* a,b:s0,s1 */ int sum(int x, int y) { return x+y; }
address (shown in decimal) 1000 mv a0,s0 # x = a 1004 mv a1,s1 # y = b 1008 addi ra,zero,1016 #ra=1016 1012 j sum #jump to sum 1016 … # next instruction … 2000 sum: add a0,a0,a1 2004 jr ra # new instr. “jump register”
Example
Notes: Code is behind white boxes
Prepare the function arguments a0, a1
RA – computation of the return address for function.
SUM result goes to a0, which is now employed for “return value”
JR – jump register

## Slide 14
... sum(a,b);... /* a,b:s0,s1 */ int sum(int x, int y) { return x+y; }
Question: Why use jr here? Why not use j?
Answer: sum might be called by many places, so we can’t return to a fixed place. The calling proc to sum must be able to say “return here” somehow.
Example
Notes: Function code re-use

## Slide 15
Single instruction to jump and save return address: jump and link (jal)
Before: 1008 addi ra,x0,1016 #ra=1016 1012 j sum #goto sum
After: 1008 jal sum # ra=1012,goto sum
Why have a jal?
  Make the common case fast: function calls very common
  Reduce program size
  Don’t have to know where code is in memory with jal!
Example (Cont.)
Notes: Additional
JAL = Jump and Link – single instruction instead of 2 we did before: saves RA and jumps
Historical Jump and Link, actually does Link and then Jump.
Don’t have to know where code is in memory with jal!  special HW will calculate RA according to current PC.

## Slide 16: Question 1
int Leaf(int g, int h, int i, int j){
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers a0, a1, a2, and a3
f in register s0
Assume we need one temporary register s1
Write the RISC-V code for Leaf
Notes: S0, S1 – just general registers in this case.
Caller who called Leaf, should save aside previous values of a0-a3, s0-s1

## Slide 17: RISC-V Code for Leaf()
Leaf: addi sp,sp,-8 # adjust stack for 2 items
sw s1, 4(sp) # save s1 for use afterwards
sw s0, 0(sp) # save s0 for use afterwards
add s0,a0,a1 # f = g + h
add s1,a2,a3 # s1 = i + j
sub a0,s0,s1 # return value (g + h) – (i + j)
lw s0, 0(sp) # restore register s0 for caller
lw s1, 4(sp) # restore register s1 for caller
addi sp,sp,8 # adjust stack to delete 2 items
jr ra # jump back to calling routine
Prologue
Epilogue
Task
Notes: S0, S1 – temp registers.
First of all save aside in stack previous values of S0, S1
Move stack pointer down
Save previous value of s0, s1
This is a Callee responsibility, since only Callee knows that it changes s0, s1
The do the functional code… return value  to a0
The first part is called “Prolog”
The last part is called “Epilog”
Delete operation: moving SP back up.

## Slide 18: Stack Before, During, After Function
We need to save old values of s0 and s1
sp
Before call
sp
Saved s1
During call
Saved s0
sp
After call
Saved s1
Saved s0

## Slide 19: What If a Function Calls a Function? Recursive Function Calls?
int fact (unsigned int n) { if (n == 0) return 1; return n * fact(n-1); }
int main() { return fact(3); }
Notes: Two cases
Function a calls function b
Function a calls function a

## Slide 20: Questions
A. (prologue main) – What is the needed space in the stack for the main?
4 bytes only (for register ra, which is about to be changed when calling fact).
B. (pre-call main) - What argument will main send to fact and how?
Before main calls fact, it stores the argument 3 to register a0.
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Notes: Two cases
Function a calls function b
Function a calls function a

## Slide 21: Questions
C. (pre-call fact(n)) - What argument will fact(n) send to fact(n-1) and how?
Before fact(n) calls fact(n-1), it stores the argument n-1 to register a0.
D. (pre-call fact(n)) - Which values has to be saved before fact(n) calls fact(n-1)?
Registers ra and a0, since they are about to be changed when calling fact(n-1).
E. What is the needed space in the stack for fact(n)?
8 bytes, for registers ra and a0.
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Notes: Two cases
Function a calls function b
Function a calls function a

## Slide 22: Questions
int fact (int n) { if (n < 1) return (1); return (n * fact(n-1)); }
main() { return (fact(3)); }
F. How many different frames will be defined in the stack?
A single frame for main and a frames for each time fact(n) is called, where n=0,1,2,3. Therefore 5 frames in total.
J. How many different values will register ra receive?
3 different values will be stored in register ra: the address of the operating system that called main the address of main that called fact(3) the (same) address of fact(n) that called fact(n-1), for n=3,2,1.
Notes: Two cases
Function a calls function b
Function a calls function a

## Slide 23
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
sp
0x bffe fffc
0x bfff 0000
sp
Frame
main
address of PC+4 of OS
0

## Slide 24
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
ra = address of PC+4 of OS
3
0x00400010
0
address of PC+4 of OS
0x bfff fffc
Frame
main
sp

## Slide 25
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
sp
0x bfff fff4
0x bfff fffc
Frame
main
ra = address of PC+4 of OS
3
0x00400010
Frame fact(n=3)
sp

## Slide 26
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
0x bfff fff4
3
0x00400010
sp
ra = 0x00400010
Frame fact(n=3)
a0 = 3
2
0x00400120

## Slide 27
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
0x bfff fff4
sp
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
2
sp
Frame fact(n=2)
ra = 0x00400120
a0 = 2
1
0x bfff ffec

## Slide 28
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
sp
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
1
sp
Frame fact(n=1)
ra = 0x00400120
a0 = 1
Frame fact(n=2)
ra = 0x00400120
a0 = 2
0
0x bfff ffe4
0x bfff ffec

## Slide 29
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
1
Frame fact(n=1)
ra = 0x00400120
a0 = 1
Frame fact(n=2)
ra = 0x00400120
a0 = 2
0
0x bfff ffe4
0x bfff ffdc
sp
sp
Frame fact(n=0)

## Slide 30
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 0
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
Frame fact(n=1)
ra = 0x00400120
a0 = 1
Frame fact(n=2)
ra = 0x00400120
a0 = 2
Frame fact(n=0)
sp
sp
1
0x bfff ffe4
0x bfff ffdc

## Slide 31
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
0x bfff ffe4
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
1
Frame fact(n=1)
ra = 0x00400120
a0 = 1
Frame fact(n=2)
ra = 0x00400120
a0 = 2
Frame fact(n=0)
sp
1
0

## Slide 32
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
Frame fact(n=1)
ra = 0x00400120
a0 = 1
Frame fact(n=2)
ra = 0x00400120
a0 = 2
sp
sp
1
0x bfff ffe4
0x bfff ffec
1

## Slide 33
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
1
Frame fact(n=2)
ra = 0x00400120
a0 = 2
1
sp
0x bfff ffec
2

## Slide 34
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
Frame fact(n=2)
ra = 0x00400120
a0 = 2
sp
sp
2
0x bfff fff4
0x bfff ffec
1

## Slide 35
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
0x00400120
3
6
0x bfff ffec
sp
2
0x00400010
2
1

## Slide 36
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
Frame fact(n=3)
ra = 0x00400010
a0 = 3
sp
sp
0x bfff fff4
0x bfff fffc
0x00400010
6
2
Return to main with $a0=6=3!

## Slide 37
int fact (unsigned int n) { if (n == 1) return (1); return n * fact(n-1); }
int main() { return fact(3); }
Address | Content | 
0x bfff 0000 |  | 
0x bffe fffc |  | 
0x bffe fff8 |  | 
0x bffe fff4 |  | 
0x bffe fff0 |  | 
0x bffe ffec |  | 
0x bffe ffe8 |  | 
0x bffe ffe4 |  | 
0x bffe ffe0 |  | 
0x bffe ffdc |  | 
Stack
Register | Content
ra | 
a0 | 
a1 | 
sp | 
Registers
Frame
main
ra = address of PC+4 of OS
sp
0x00400010
6
2
0x bfff fffc
address of PC+4 of OS
sp
0x bfff 0000

## Slide 38
Notes: There is one more table, See the pdf

## Slide 39: Questions
int fact (int n) { if (n < 1) return (1); return (n * fact(n-1)); }
main() { return (fact(3)); }
Draw all necessary arrows to complete the flow of the previous code (program):
main
Prologue
Pre-call
Post-call
Epilogue
fact(n=3)
Prologue
Pre-call
Post-call
Epilogue
fact(n=2)
Prologue
Pre-call
Post-call
Epilogue
fact(n=1)
Prologue
Pre-call
Post-call
Epilogue
fact(n=0)
Prologue
Epilogue
Notes: Two cases
Function a calls function b
Function a calls function a

## Slide 40
שאלה ממבחן – תשע"ט חורף מועד א'

## Slide 41
שאלה ממבחן – תשע"ט חורף מועד א'
1
2
3
4
lui s0, 0x20
ra
add a0, x0, s0
ra

## Slide 42
שאלה ממבחן – תשע"ט חורף מועד א'
האם הקוד מקיים קונבנציית הקריאה לפונקציה? הסבר. אם לא, תאר אילו שינויים נדרשים על מנת שהקוד ירוץ לפי הקונבנציה.
על מנת שהפונקציה תרוץ לפי קונבנציית הקריאה לפונקציה, נדרש:
לגבות את s2,s1,s0 בתחילת הריצה, ולהחזיר אותם לערך הראשוני בסוף הריצה.
לשחרר את המחסנית בסוף התוכנית.